| L100C-24 25.9V（7Serial）Li-Ion Battery pack charger |
| --- |
|  | ITEM | UNIT | SPECIFICATION | REMARK |
| INPUT |
| 01 | Rating Input Voltage | V ac | 100~240Vac 50/60Hz |  |
| 02 | Input voltage range | V ac | 90~264Vac |  |
| 03 | Rating Input Current | A | 1.3Arms | INPUT:220V OUTPUT:Full load |
| 04 | Max. input power | W | 100 |  |
| OUTPUT |
| 05 | Rating output voltage | V dc | 29.4V |  |
| 06 | Output voltage range | V dc | 20VDC ~ 29.4VDC |  |
| 07 | Suit with Battery type |  | 25.9V（7Serial）4~12Ah Li-Ion |  |
| 08 | Charging current | A | 2.8( 0.15@41V |  |
| 09 | Charging voltage | V | 29.4V +-0.1V |  |
| 10 | Cut-off current | A | 0.10~0.2A |  |
| 11 | Typical charging time | hour |  | For 8000mAH |
| 12 | Max. output power | W | 85W |  |
| 13 | Hold-on time | ms | NC | Input: 220Vac Output: Full load |
| 14 | Ripple current(RMS) | mA | 100 | Input: 220Vac Output: Full load |
| 15 | Charge finish condition |  | V>29V + I<0.2A |  |
| 16 | LED color |  | Red: charging Green: finish/idle |  |
| 17 | Output protect | - | OCP & OVP |  |
| 18 | Efficiency | % | 85% | At max. load |
| Environment |
| 19 | Operate temperature | °C | -10 ~ +40 | Full load & natural convection. |
| 20 | Operate humidity | %RH | < +90 | Relative humidity, non-condensing. |
| 21 | Storage temperature | °C | -40 ~ +70 |  |
| 22 | Storage humidity | %RH | 0 ~ +95 | Relative humidity, non-condensing. |
| 23 | Cooling | - | Natural convection |  |
| 24 | Temperature factor | % | -- |  |
| 25 | Vibration resistance |  | 5MM/50HZ/600S | Non-operating condition. |
| 26 | Impact resistance |  | 1 meter drop test >= 3 times | Non-operating condition. |
| Mechanical |
| 27 | Weight | g | 650 |  |
| 28 | Size | mm | 170X71X51 | Casing only |
| 29 | Connectors | - | Defined when order |  |
| Safety |
| 30 | Max. temperature rise | °C | < 40 on casing | At any line and Max. Load |
| 31 | Safety standards | - | EN60335-2-29 UL1310 |  |
| 32 | EMC standard | - | EN55014 |  |
| 33 | MTBF | hrs | 30000 |  |
| 34 | Limited power source | VA | - |  |
| 35 | ESD | kV | 8.0 |  |
| 36 | Hi-Pot Insulation | V | i/p to o/p: 3000 (1 min.) | For final unit, cut-off current =10mA |